## Slide 1: IETF Network Slice Topology YANG Data Model
Co-authors:
Xufeng Liu (IBM)
Jeff Tantsura (Microsoft)
Igor Bryskin (Individual)
Luis M. Contreras (Telefonica)
Qin Wu (Huawei)
draft-liu-teas-transport-network-slice-yang-06
Sergio Belotti (Nokia)
Reza Rokui (Ciena)
Aihua Guo (Futurewei)
Italo Busi (Huawei)

## Slide 2: Motivation
A network slice may demand additional level of control to customize its connections, as described in Section 2 of draft-ietf-teas-ietf-network-slices
  “Additionally, the IETF Network Slice service customer might ask for some level of control of, e.g., to customize the service paths in a network slice.”
A network slice can benefit from using a customized topology to allow better resource sharing among the connections
  “network slice topology”
A network slice topology expresses the slice customer’s intent with customer-oriented SLO/SLEs
  Existing topology models, e.g. network topology or TE topology is neither intent-oriented nor contains the SLO/SLEs needed from customer’s perspective
The network slice topology can be either technology-agnostic or technology-specific depending on the specific network slice to be built
A network slice may reference a network slice topology and build explicit path for its connections

## Slide 3: Clarification of Terminologies
Native MDSC topology: topology resources managed by the MDSC (internal topology)
Abstract topology: an abstraction of the network topology resources, exposed by the MDSC at its NBI (topology discovery)
Customized topology: the customer intent for reserving topology resources within the network and express connectivity constraints
--> what we need for network slicing is the customized topology and NOT the abstract topology

## Slide 4: Reusing Existing Model for Network Slice Topologies
draft-liu-teas-transport-network-slice-yang-05 originally exists to represent and configure a network slice as a topology
  The SLO/SLE attributes for topological resources need to align with what is defined in the network slice framework & ns-nbi YANG model
  No need to augment TE models to model connectivity constraints (they are covered by the ns-nbi YANG model)

## Slide 5: Model Relationships

## Slide 6: Model Tree
Network augments
Node augments

## Slide 7: Model Tree
Link augments
TP augments

## Slide 8: Open Issue
Should the NS-NBI model reference this topology model, or any topology model?
  Restrain that the topology to be reference is of type “network-slice”

## Slide 9: Next Steps
Resolve open issues
Request for WG adoption
* GitHub Repo
  https://github.com/aguoietf/ietf-network-slice-topology

## Slide 10
Thank You!