## Slide 1: WT-411i2 & WT-454i2 Considerations on Inventory & Topology
Haomian Zheng, Guoxiang Liu, Aihua Guo
May 30, 2023

## Slide 2: Take-aways in C
Several sources suggest to reference a network equipment inventory from the network topology physical infrastructure layer
IETF Network HW inventory looks like a good reference for BBF equipment inventory TR 454 i2
  Support and would like to start with “draft-ietf-ccamp-network-inventory-yang”, and feedback to IETF if we find any comments;
  To clarify the relationship with the current ‘bbf-equipment-inventory’ and ‘bbf-network-map’, an overwrite?;
  Only network HW ( TR 454 EI also include pAN, (=PMA for access node))
  Includes also node HW sub-components (chassis, slots, boards, cages) ( TR 454 EI)
  Does not include home devices ( TR 454 EI)
  draft-ietf-ccamp-network-inventory-yang defines a generic and hierarchical definition which in general also support home devices with new type definition. Technology-specific inventory attributes can be extended for ONU, AP, STA, ODN, see more details in the following pages.
We might also refer to multiple OSS subsystems NB of Access SDN M&C which represents reality (not only CloudCO DO)
  Clarification: any example scenario?
Reference: https://wiki.broadband-forum.org/download/attachments/204472806/Inventory-Topology_4_17_2023.pptx?version=1&modificationDate=1681906477816&api=v2

## Slide 3: Proposed Model Structures
ietf-network-hardware-inventory defines a network-scope inventory model. It contains generic definitions for inventory objects as well as their hierarchical parent-child relationships.
  Network element, chassis, card, port, link can be reused for access networks
Augmented inventory models for PON and home devices:
Inventory YANG model for ONU – defines ONU network-level inventory parameters for multiple PON types
Home gateway YANG model – defines service-level inventory parameters for home gateways
  Used when the home gateway is separate from the ONU
Access point YANG model – defines inventory YANG models for Wi-Fi AP
ietf-network-hardware-inventory
ONU Augmentation
Others...
Home Gateway
Augmentation
Access Point
Augmentation

## Slide 4: ONU Inventory Model
Augments the ietf-network-hardware-inventory
  Inherits common/generic attributes for inventory objects from the base model
  Reuses common ONU attributes defined in the common YANG models
  Consideration: need to align common attributes defined in the above two models
Key features in ONU Augmentations
  Add ONU specific attributes for different PON types
    Consideration: evaluate whether these ONU attributes are defined in separate containers or defined under the common container in ietf-network-hardware-inventory
  Supports …

## Slide 5: ONU Model Tree (Sample)
network-element : OLT
ONU
+--:(pon-port)
| +--ro pon-port-specific-info
+--:(onu)
+--ro down-bw?
+--ro ref-parent-ltp
+--ro pon-type
+--ro loid
+--ro voip-address
+--ro onu-id
+--ro fttx-mode
+--ro mac-address
+--ro onu-class
+--ro onu-type
+--ro bandwidth-type
+--ro terminal-type
+--ro tags
Sample :
ONU specific attributes
ONU component attributes
Common reusable attributes
OLTboardPON port-->ONU

## Slide 6: Home Gateway Inventory Model
Augments the ietf-network-hardware-inventory
  Inherits common/generic attributes for inventory objects from the base model
  Reuses common ONU attributes defined in the common YANG models per TR-383
  Consideration: need to align common attributes defined in the above two models
Key features in home gateway augmentations
  Definition of home gateway models

## Slide 7: Home Gateway Model Tree (Sample)
...
|
+--ro home-gw
+--ro model?
Specific attributes for home gateways

## Slide 8: Wi-Fi AP Inventory Model
Augments the ietf-network-hardware-inventory
  Inherits common/generic attributes for inventory objects from the base model
  Reuses common ONU attributes defined in the common YANG models
  Consideration: need to align common attributes defined in the above two models
Key features in the augmentations
  Common reusable grouping definition for APs
    ssid-info, neighbor-ssid-info
    uplink-pon-info
    common-error-info
  Extensible opaque attribute for vendor implementation
  Definition for supported Wi-Fi bands
  Definition for connected home devices

## Slide 9: Summary
Augmented inventory data models for ONUs based on ietf-network-hardware-inventory
Reuse common attributes from the IETF base model and common YANG models