## Slide 1: Delivery of Premium Services with Multi-technology Network Slicing
Aihua Guo, Principal Architect
UFBB BASe 2022
2022-09-09

## Slide 2
Network Vision : Fiber to Everywhere, Enabling All Industries
Device/Machine
Campus/Verticals
Home/Business
Data Centre (Core, Backbone, Metro, etc.)
FTTH -> FTTR
FTTO->FTTD
FTTC->FTTM
OTN extending CO -> Site
1000KM
10KM
1KM
10M
1M
Fiber to everywhere, end to end (FTTx, optical to cloud)
Extending reach to more end users : 2Home/Room/Business/Consumer/Mobile/Device/Machine
Massive number of connections: x3 (room), x10(desk), x30(machine), x100(smart city)

## Slide 3
Main Features for Extending and Enhancing Fixed Networks
//////
Fiber To
Everywhere
eFBB
RRL
GRE
OPS
FFC
GON
10GPON  50G PON
200/400G  800G
1G OTN  Sub-1G OSU
WIFI 6  WIFI 6e/7
Field-bus Control System
Energy/Transport Control and Communications
Native Hard Pipe (Jitter, Packet loss…)
Premium Broadband
Premium Private Line
Ultra-low Latency
Autonomous Networking (AND L3  L4 )
Fiber Positioning and Visualization
Fiber Digitalization
FTTHome  FTTRoom
FTTOffice  FTTDesk
FTTFactory  FTTMachine
Optical to the Site
One-hop to Cloud
Optical Switching
Green Optical Network
Optical Precise Sensing
Realtime Reliable Link
Reference: ETSI F5G Network Architecture

## Slide 4
Enabling Premium Services with Full Fiber Connectivity
Gaming Cloud
VR education cloud
GW
GW
OLT1
OLT2
OLT800
...
OLTXXX
...
ONT
ONT
ONT
ONT
2H scenario: CloudVR/All-optical gold pipe
High performance channel through home, access and metro network
Dynamic channel driven by VR applications
Efficient resource utilization
Headquarters
branching
Headquarters
branching
Cloud Optical Network
Boutique
Public cloud
Industry cloud
Private Cloud
VPN
2B scenario: High Quality Private Line
Hard isolation among different services
High availability
2B scenario: Multi-cloud enterprise private line
End-to-end QoE assurance
Multi-cloud access
Service awareness and service driven

## Slide 5
End-to-end Management and Control
Management Layer
Orchestration Layer
OLT
OTN
Cloud/
Local DC
DC GW
Customer Premises Network
Access Network
Aggregation Network
Core Network
AggN
Edge
'
OTN
Edge
XC
OTN-CPE
E
-
CPE
E
-
CPE
CPN
-
A
RG
ONU
WG
ONU
CE
ONU
CE
ONU
IE
FTTR
Core
Network
Core PE
IP/Eth AggN
IP Controller
AN Controller
CPN Controller
AN Controller
AggN Controller
CN Controller
E2E Service Orchestrator
CPN NBI
AN NBI
AggrN NBI
CN NBI
Intent
CPN SBI
AN SBI
IP SBI
OTN SBI
CN SBI
Network Layer
(ASON+/OSP)
Unified management & control across multi-technology domains
Standard, open interfaces ensuring multi-vendor interoperability

## Slide 6
Realizing Premium Services with End-to-end Network Slicing
Intent driven
Differentiated services on a shared infrastructure with different technology domains
Customized network partitioning with OAM based on customer requirements
Network service self-containment and isolation
Guaranteed / Deterministic QoS
L0 Slice
AN Slice
Best effort
OTN Slice
IP Slice
DC Slice
Medium Quality
Premium Quality
OTN Slice Controller
CPN Slice
Controller
AN Slice
Controller
IP Slice Controller
CN Controller
E2E Slice Orchestrator
CPN NBI
AN NBI
IP NBI
CN NBI
Intent
OTN NBI

## Slide 7
Hierarchical Slice Control: IETF ACTN Architecture
Abstraction and Control of Traffic-engineered Networks (ACTN): solution for hierarchical network slice management
Open YANG-based data models for technology-agnostic slicing and technology-specific slicing, e.g. IP, OTN, L0, Microwave
IP Slice
OTN E2E Slice
OTN Slice – Domain 1
OTN Slice – Domain 2
L0 Slice – Domain A
L0 Slice – Domain B
L0 Slice – Domain C
L0 Slice – Domain D

## Slide 8: Standards: IETF YANG Data Models for ACTN and Slicing
ACTN Arch. & Info Model
RFC / RFC process
WG
ID
ACTN NBI YANG model Applicability
ACTN framework RFC8453
ACTN Info Model RFC8454
MW SDN framework RFC8432
Others
Service Models @ CMI&MPI
Network Models @ MPI
Network Topo RFC8345
WDM topo
Flex-grid topo
OTN topo
Non-TE L2 topo
L3 topo RFC8346
WDM tunnel
Flex-grid
tunnel
OTN tunnel
L2SM RFC8466
TE Tunnel
VN Service
L3SM RFC8049
Topology Model
Tunnel Model
L0
L1
L2 TE
L2
Non-TE
MW
L3
Other Model
Alarm model RFC8632
Telemetry
MW topo
MW config RFC8561
ETH/Client Tunnel
ETH TE topo
L1CSM
L1 Client service
TE Service mapping
Path
Computation
Model
Path Computation
CMI Service Model
MPI Service Model
TE types RFC8776
Generic OAM model RFC8351
ETH Service
L1 types
L0 types
OIA topo
TE Topo
Network Slicing
IETF Network Slicing Framework
OTN Slicing
IP Network Slicing

## Slide 9
Access Network Slicing: BBF FAN Sharing and Data Models
NSI2
NSI1
NETCONF/YANG
D-Net1
OLT
D-Net1
NSI2
NSI1
NSI2
NSI4
NSI3
D-Net2
D-Net2
NSI4
NSI3
NSI2
NSI1
NSI4
NSI3
NSI2
NSI1
NSI4
NSI3
ONT
D-NET1
D-NET2
NNI
WIFI
RU
OMCI
SDN Controller
Mgmt Slice 1
NSIY
NSIX
D-Net0
NSIY
NSIX
NSIY
NSIX
NSIY
NSIX
D-NET0
NSI 1
NSI 2
D-Net1
NSI 1
NSI 2
D-Net1
D-Net2
NSI 3
NSI 4
D-Net2
Mgmt Slice 2
D-Net0
NSI Y
D-Net0
NSI X
Mgmt Slice0
OSS / Slicing Management
D-Net0
RESTCONF/YANG
User 1
User 2
User 3
OSS 2
OSS 1

## Slide 10
PoC Demo: Cloud VR Premium Services
MA5800
OSN9800
OSN9800
ONT1
ONT2
Cloud VR Server
DC GW
OTN Slice
OLT
OA
OE
Optical Transport Controller
Wi-Fi 6
10GPON
User 1 starts a first VR application, triggering the OTN slice creation (with one OTN connection)
User 2 starts a second VR application, triggering the OTN connection BW increasing
User 1 terminates his VR application, triggering the OTN connection BW decreasing
User 2 terminates his VR application, triggering the OTN connection deletion
0) Service protocol
User/cloud address learning
3) VR BW request
3) VR BW request
4) Connection Protocol
OTN connection creation / BW modification
Demo Steps
* The multi-cloud case will be supported in phase2, wherein the OTN needs to sense the multiple users/clouds, and map different traffics into correct OTN connections
Cloud VR Server
DC GW
Phase 2 Demo*
1) Get VR server address
2) VR app identification

## Slide 11
PoC Demo: Closed-loop Automation
Physical network controller (domain B)
Physical network controller (domain A)
ONAP Orchestrator
(IBN framework)
Physical network domain A
Physical network domain B
DC
Campus network
Campus network
IETF/ACTN Interface
Closed-loop Automation
Slice User
User Intent Interface

## Slide 12: Summary
Fiber-to-everywhere makes the network infrastructure future proof
  Wider reach to massive end users, larger bandwidth for access & transport, fine granular OTN
End-to-end management and control is a key component for service delivery across multi-technology domains
Network slicing enables the provisioning of premium services with flexible resource isolation and guaranteed performance across CPN, Access, Aggregation and Core/DC networks