## Slide 1: WT-411i2 & WT-454i2 Considerations on Inventory & Topology
Haomian Zheng, Guoxiang Liu
May 30, 2023

## Slide 2
Background Information from Nokia Starts here...

## Slide 3: Equipment Inventory and Topology in BBF TR-454
BBF equipment inventory
  BBF-defined YANG module, listing three “sub-” inventories:
    (Network) devices (PNFs)
      with optional HW, management and SW information
    pANs: virtual representation of AN PNFs (=PMA representation) with leaf-ref to device
      With attributes related to datastore (model, alignment), admin state, device –adapters (BAA)
    End-user devices
      HW, management and SW info attributes
BBF network map
  Uses ietf-network-topology with several augmentations
    E.g. geo/site/responsible information augmentation for the network nodes
  Leaf references to “BBF Equipment inventory” YANG module for “node ID” and “end-user-device-ID”
  Enables to link network nodes with each other without using ietf-network-topology “link” and “termination point” definitions, instead leveraging “deployment topology”/“connected node” augmentation for nodes
Both Inventory and network map are defined for “CloudCO’s Northbound API”
  No explicit reference to TR 411 Occo-Nf-sdn-access (CloudCO DO –Access SDN M&C interface)

## Slide 4
Augment network
bbf-network-map
bbf-equipment-inventory
TR-454
rw: for configuration data nodes and choice nodes
TR 451: “the data provided by the models in this TR (454) can be exposed to management systems through the CloudCO's Northbound API as is; as a reduced set of instance data or data elements; abstracted into a different Network Map or Equipment inventory model representation”
ro: for non-configuration data nodes and choice nodes, output parameters to rpcs and actions, and notification parameter
(RFC 8340, YANG Tree Diagrams)
Ietf-network
Ietf-network-topology
TR-454
RFC 8345
module: ietf-network
+--rw networks
+--rw network* [network-id]
+--rw network-id network-id
+--rw network-types
+--rw supporting-network* [network-ref]
| +--rw network-ref -> /networks/network/network-id
+--rw node* [node-id]
+--rw node-id node-id
+--rw supporting-node* [network-ref node-ref]
+--rw network-ref -> ../../../supporting-network/network-ref
+--rw node-ref -> /networks/network/node/node-id
module: ietf-network-topology
augment /nw:networks/nw:network:
+--rw link* [link-id]
+--rw link-id link-id
+--rw source
| +--rw source-node? -> ../../../nw:node/node-id
| +--rw source-tp? -> ../../../nw:node[nw:node-id=current()/../source-node]/termination-point/tp-id
+--rw destination
| +--rw dest-node? -> ../../../nw:node/node-id
| +--rw dest-tp? -> ../../../nw:node[nw:node-id=current()/../dest-node]/termination-point/tp-id
+--rw supporting-link* [network-ref link-ref]
+--rw network-ref -> ../../../nw:supporting-network/network-ref
+--rw link-ref -> /nw:networks/network[nw:network-id=current()/../network-ref]/link/link-id
augment /nw:networks/nw:network/nw:node:
+--rw termination-point* [tp-id]
+--rw tp-id tp-id
+--rw supporting-termination-point* [network-ref node-ref tp-ref]
+--rw network-ref -> ../../../nw:supporting-node/network-ref
+--rw node-ref -> ../../../nw:supporting-node/node-ref
+--rw tp-ref -> /nw:networks/network[nw:network-id=current()/../network-ref]/node[nw:node-id=current()/../node-ref]/termination-point/tp-id
import
Augment node
Leafref, referring to device id defined in equipment-inventory for network devices and end-user devices under node
network
-supporting network
-node
-supporting node
import
Augment termination point
network
-supporting network
-node
-supporting node
-termination point
-supporting termination point
-link
-supporting link
Augment network
Leaf Tenant-ID
Augment node

## Slide 5: RFC 8345

## Slide 6: TR-454
module: bbf-equipment-inventory
+--ro equipment-inventory {bbf-inv:reports-equipment-inventory}?
+--ro device-inventory {bbf-inv:reports-device-inventory}?
| +--ro device* [device-id]
| +--ro device-id string
| +--ro hardware-info
| | +--ro device-type? identityref
| | +--ro serial-num? bbf-yang:string-ascii64
| | +--ro mfg-name? bbf-yang:string-ascii64
| | +--ro model-name? bbf-yang:string-ascii64
| +--ro management-info
| | +--ro ip-address? inet:host
| | +--ro port? inet:port-number
| | +--ro admin-state? bbf-nodet:admin-state
| +--ro software-info
| +--ro software-instance* [software-type current-revision]
| +--ro software-type identityref
| +--ro current-revision bbf-yang:string-ascii64
| +--ro previous-revision? bbf-yang:string-ascii64
| +--ro current-revision-last-changed? yang:date-and-time
+--ro pan-info {bbf-inv:reports-baa-pan-inventory}?
| +--ro pan-instance* [pan-id]
| +--ro pan-id bbf-yang:string-ascii64
| +--ro device-ref? -> /equipment-inventory/device-inventory/device/device-id {bbf-inv:reports-device-inventory}?
| +--ro admin-state? bbf-node-types:admin-state
| +--ro admin-state-change-timestamp? yang:date-and-time
| +--ro datastore
| | +--ro metamodel* string
| | +--ro metamodel-alignment-state? bbf-node-types:alignment-state
| | +--ro schema-update-timestamp? yang:date-and-time
| | +--ro an-alignment-state? bbf-node-types:alignment-state
| | +--ro an-alignment-state-change-timestamp? yang:date-and-time
| +--ro device-adapter
| +--ro software-type? identityref
| +--ro current-revision? bbf-yang:string-ascii64
| +--ro previous-revision? bbf-yang:string-ascii64
| +--ro current-revision-last-changed? yang:date-and-time
| +--ro alignment-state-update-timestamp? yang:date-and-time
+--ro eud-inventory {bbf-inv:reports-end-user-device-inventory}?
+--ro eud-equipment* [eud-id]
+--ro eud-id string
+--ro hardware-info
| +--ro device-type? identityref
| +--ro serial-num? bbf-yang:string-ascii64
| +--ro mfg-name? bbf-yang:string-ascii64
| +--ro model-name? bbf-yang:string-ascii64
+--ro management-info
| +--ro ip-address? inet:host
| +--ro port? inet:port-number
| +--ro admin-state? bbf-nodet:admin-state
+--ro software-info
+--ro software-instance* [software-type current-revision]
+--ro software-type identityref
+--ro current-revision bbf-yang:string-ascii64
+--ro previous-revision? bbf-yang:string-ascii64
+--ro current-revision-last-changed? yang:date-and-time
module: bbf-network-map
augment /nw:networks/nw:network:
+--rw tenant-id? string {bbf-nm:reports-network-map}?
augment /nw:networks/nw:network/nw:node:
+--rw node-type? identityref {bbf-nm:reports-network-map}?
+--rw network-device-properties {bbf-nm:reports-network-map}?
| +--rw alias? bbf-yang:string-ascii64
| +--rw device-ref? -> /bbf-inv:equipment-inventory/device-inventory/device/device-id {bbf-inv:reports-equipment-inventory,bbf-inv:reports-device-inventory}?
+--rw enduser-device-properties {bbf-nm:reports-network-map}?
| +--rw end-users
| | +--rw end-user* [end-user-id]
| | +--rw end-user-id bbf-yang:string-ascii64
| | +--rw given-name? bbf-yang:string-ascii64
| | +--rw family-name? bbf-yang:string-ascii64
| | +--rw contact* [type]
| | +--rw type bbf-yang:string-ascii64
| | +--rw value? bbf-yang:string-ascii64
| +--rw device-ref? -> /bbf-inv:equipment-inventory/eud-inventory/eud-equipment/eud-id {bbf-inv:reports-equipment-inventory,bbf-inv:reports-end-user-device-inventory}?
+--rw geographic-location {bbf-nm:reports-network-map}?
| +--rw civic-address
| | +--rw civic-address* [label value]
| | +--rw label enumeration
| | +--rw value string
| +--rw wgs84-location {bbf-loc:wgs84-location-support}?
| +--rw latitude? string
| +--rw longitude? string
+--rw responsible-party-contact {bbf-nm:reports-network-map}?
| +--rw given-name? bbf-yang:string-ascii64
| +--rw family-name? bbf-yang:string-ascii64
| +--rw contact* [type]
| +--rw type bbf-yang:string-ascii64
| +--rw value? bbf-yang:string-ascii64
+--rw site {bbf-nm:reports-network-map}?
| +--rw site-type? identityref
| +--rw plant-type? identityref
| +--rw building? bbf-yang:string-ascii64
| +--rw floor? bbf-yang:string-ascii64
| +--rw room? bbf-yang:string-ascii64
| +--rw line? uint16
| +--rw rack-position? uint16
| +--rw frame-position? uint16
+--rw deployment-topology {bbf-nm:reports-network-map}?
+--rw deployment-type? identityref
+--rw connected-node* [network-ref node-ref]
+--rw network-ref -> /nw:networks/network/supporting-network/network-ref
+--rw node-ref -> /nw:networks/network/node/node-id
augment /nw:networks/nw:network/nw:node/nt:termination-point:
+--rw distribution-frame-type? identityref {bbf-nm:reports-network-map}?
+--rw geographic-location {bbf-nm:reports-network-map}?
+--rw civic-address
| +--rw civic-address* [label value]
| +--rw label enumeration
| +--rw value string
+--rw wgs84-location {bbf-loc:wgs84-location-support}?
+--rw latitude? string
+--rw longitude? string
Allows to specify which nodes interconnect with each other,
Without using the link and termination point node definitions of “ietf-network-topology”

## Slide 7: draft-ietf-ccamp-network-inventory-yang-01 A YANG Data Model for Network Hardware Inventory
[RFC8345] initial goal was to make possible the augmentation of the YANG data model with network hardware inventory data model but this was never developed and the scope was kept limited to network topology data only.
It is key for operators to drive the industry towards the use of a standard YANG data model for network hardware inventory data instead of using vendors proprietary APIs (e.g., REST API).
[RFC8348] defines a YANG data model for the management of the hardware on a single server and therefore it is more applicable to the domain controller South Bound Interface (SBI) towards the network elements rather than at the domain controller's northbound. However, the YANG data model defined in [RFC8348] has been used as a reference for defining the YANG network hardware inventory data model presented in this draft.
Network Hardware Inventory in IETF

## Slide 8: draft-ietf-ccamp-network-inventory-yang-01 A YANG Data Model for Network Hardware Inventory
 | ietf-network-hardware-inventory (prefix ni)

## Slide 9: draft-ietf-ccamp-network-inventory-yang-01 A YANG Data Model for Network Hardware Inventory

## Slide 10: draft-ietf-ccamp-network-inventory-yang-01 A YANG Data Model for Network Hardware Inventory
uuid of a network element in ietf-network-hardware-inventory
uuid of a port component in ietf-network-hardware-inventory

## Slide 11: RFC 8348 A YANG Data Model for Hardware Management

## Slide 12
Background Information from Nokia ends here...

## Slide 13: Take-aways in C
Several sources suggest to reference a network equipment inventory from the network topology physical infrastructure layer
IETF Network HW inventory looks like a good reference for BBF equipment inventory TR 454 i2
  (Haomian) Support and would like to start with “draft-ietf-ccamp-network-inventory-yang”, and feedback to IETF if we find any comments;
  (Haomian) To clarify the relationship with the current ‘bbf-equipment-inventory’ and ‘bbf-network-map’, an overwrite?;
  Only network HW ( TR 454 EI also include pAN, (=PMA for access node))
  Includes also node HW sub-components (chassis, slots, boards, cages) ( TR 454 EI)
  Does not include home devices ( TR 454 EI)
  (Haomian) draft-ietf-ccamp-network-inventory-yang defines a generic and hierarchical definition which in general also support home devices with new type definition. Technology-specific inventory attributes can be extended for ONU, AP, STA, ODN, see more details in the following pages.
We might also refer to multiple OSS subsystems NB of Access SDN M&C which represents reality (not only CloudCO DO)
  (Haomian) Any example scenario?
Reference: https://wiki.broadband-forum.org/download/attachments/204472806/Inventory-Topology_4_17_2023.pptx?version=1&modificationDate=1681906477816&api=v2

## Slide 14: Proposed Model Structures
ietf-network-hardware-inventory defines a network-scope inventory model. It contains generic definitions for inventory objects as well as their hierarchical parent-child relationships.
Augmented inventory models for PON and home devices:
Inventory YANG model for ONU – defines ONU network-facing inventory parameters for multiple PON types
Home gateway YANG model – defines user-facing inventory parameters for home gateways
  Consideration: can we merge ONU inventory with home gateway?
Access point YANG model – defines inventory YANG models for Wi-Fi AP
ietf-network-hardware-inventory
ONU Augmentation
Others...
Home Gateway
Augmentation
Access Point
Augmentation

## Slide 15: ONU Inventory Model
Augments the ietf-network-hardware-inventory
  Inherits common/generic attributes for inventory objects from the base model
  Reuses common ONU attributes defined in the common YANG models per TR-383
  Consideration: need to align common attributes defined in the above two models
Key features in ONU Augmentations
  Add ONU specific attributes for different PON types
    Consideration: evaluate whether these ONU attributes are defined in separate containers or defined under the common container in ietf-network-hardware-inventory
  Supports different FTTx modes
  Supports different terminal types

## Slide 16: ONU Model Tree (Sample)
network-element : ONU
ONU components: ports, links
+--:(onu-port)
| +--ro onu-port-specific-info
+--:(onu-link)
+--ro onu-link-specific-info
...
|
+--ro onu
+--ro down-bw?
+--ro ref-parent-ltp
+--ro pon-type
+--ro loid
+--ro voip-address
+--ro onu-id
+--ro fttx-mode
+--ro mac-address
+--ro onu-class
+--ro onu-type
+--ro bandwidth-type
+--ro terminal-type
+--ro tags
ONU specific attributes
ONU component attributes
Common reusable attributes

## Slide 17: Home Gateway Inventory Model
Augments the ietf-network-hardware-inventory
  Inherits common/generic attributes for inventory objects from the base model
  Reuses common ONU attributes defined in the common YANG models per TR-383
  Consideration: need to align common attributes defined in the above two models
Key features in home gateway augmentations
  Definition of home gateway models

## Slide 18: Home Gateway Model Tree (Sample)
network-element : home-gw
Home gateway components?
+--:(home-gw)
| +--ro home-gw-specific-info
...
|
+--ro home-gw
+--ro model?
Specific attributes for home gateways
home gateway component attributes
Common reusable attributes

## Slide 19: Wi-Fi AP Inventory Model
Augments the ietf-network-hardware-inventory
  Inherits common/generic attributes for inventory objects from the base model
  Reuses common ONU attributes defined in the common YANG models per TR-383
  Consideration: need to align common attributes defined in the above two models
Key features in the augmentations
  Common reusable grouping definition for APs
    ssid-info, neighbor-ssid-info
    uplink-pon-info
    common-error-info
  Extensible opaque attribute for vendor implementation
  Definition for supported Wi-Fi bands
  Definition for connected home devices

## Slide 20: Wi-Fi AP Model Tree (Sample)
network-element : wifi-ap
AP components
...
|
+--ro home-ap
+--ro ap-info
| +--ro ap-list* [mac]
| +--ro mac?
| +--ro manufacture-oui?
| +--ro wifi-band-capability?
| +--ro standard-capability?
| +--ro up-link?
| +--ro work-mode?
| +--ro uplink-pon
| | +--ro transmitting-power?
| | ...
| +--ro additional-info* [name]
| +--ro name?
| +--ro value
+--ro wifi-band
+--ro mac?
+--ro radio-type?
+--ro auto-channel?
+--ro channels*
+--ro channels-in-use*
+--ro ssid-list* [ssid-index]
Specific attributes for APs
Common reusable attributes

## Slide 21: Summary
Augmented inventory data models for ONUs, home gateways and Wi-Fi APs based on ietf-network-hardware-inventory
Reuse common attributes from the base model and TR-383