## Slide 1: IETF Network Slice Topology YANG Data Model
Co-authors:
Xufeng Liu (Alef Edge)
Jeff Tantsura (Microsoft)
Igor Bryskin (Individual)
Luis M. Contreras (Telefonica)
Qin Wu (Huawei)
draft-liu-teas-transport-network-slice-yang-07
Sergio Belotti (Nokia)
Reza Rokui (Ciena)
Aihua Guo (Futurewei)
Italo Busi (Huawei)

## Slide 2: Updates since IETF-118 (1)
Change customized topologies into customer intent topology
  Represent a better way to express resource reservation preference
  The topology is provided by customer not exposed by service provider
Relationship with TE-based Topology
  Using multi-inheritance the model can be combined with other TE topology models even technology-specific, allowing the creation of customer intent topology tailored to specific requirement
Relationship with SAP Topology  2 distinct purposes
  SAP model is exposing to customer an abstract view of the provider NW including a list of Service Attachment Point(SAP) where customer service can be connected.
  In contrast customer intent topology captures a customer's intentions and provider act as the recipient of these intents

## Slide 3: Updates since IETF-118 (2)
Relationship with ACTN VN
  [I-D.ietf-teas-ietf-network-slices] defining IETF NS as collection of connectivity-constructs strictly recall the VN type 1 definition of VN + VN
  [I-D.ietf-teas-ietf-network-slice-nbi-yang] adding a reference to a customer intent topology strictly recal the VN type 2 but without specifying the explicit use of the topology
  This model is complementing what described in [I-D.ietf-teas-ietf-network-slice-nbi-yang] giving the possibility to customer to define intent topology tailored for their network slices

## Slide 4
Thank You!