## Slide 1: A YANG Data Model for WDM Tunnels
Co-authors:
Aihua Guo (Futurewei)
Sergio Belotti (Nokia)
G. Galimberti (Individual)
J.E.L.d.V. Mendez (Naudit HPCN)
D.P. Burrero (Universidad Autonoma de Madrid)
Contributors:
Daniel King (Olddog Consulting)
Haomian Zheng (Huawei)
Italo Busi (Huawei)
Victor Lopez (Nokia)
draft-ietf-ccamp-wdm-tunnel-yang-01
Contributors:
Dieter Beller (Nokia)
Ricard Vilalta (CTTC)
Young Lee (Samsung)
Bin Yeong Yoon (ETRI)
Daniel Michaud Vallinoto (Universidad Autonoma de Madrid)
Zafar Ali (Cisco)
Esther Le Rouzic (Orange)
Julien Meuric (Orange)
Gert Grammel (Juniper)
Roberto Manzotti (Cisco)
IETF 119, Brisbane

## Slide 2: Summary of Updates in -01 Rev.
Focused on YANG model updates. Cosmetic updates on the text.
YANG model updates:
  Added under transceiver constraints additional optional parameters to further constraints the transceiver configurations. Examples: constraints line coding bitrates, tx channel power and preferred rx channel power.
    The transceiver constraints can be applied globally to a WDM tunnel and/or more specifically to a source, destination or 3R regen node used by the tunnel
  Picked up updates from RFC9093-bis for removing obsolete WDM tunnel constraints and updating types for some power parameters
  Added descriptions to clarify the use of path-in-transceiver and path-out-transceivers in the scenario of starting/terminating and 3R regen
  Aligned with latest ietf-te updates and fixed compilation error on relevant augments in this model

## Slide 3: Transceiver Parameters
Unified transceiver specifications for both local transponders and integrated remote transponders
Transceiver configurations are aligned with draft-ietf-ccamp-optical-impairment-topology
augment /te:te/te:tunnels/te:tunnel:
+--rw wdm-constraint
+--rw transceiver-constraint
| +--rw operational-modes* string
| +--rw tx-tune-constraints
| | +--rw min-central-frequency? frequency-thz
| | +--rw max-central-frequency? frequency-thz
| | +--rw transceiver-tunability? frequency-ghz
| +--rw line-coding-bitrate* identityref
| +--rw tx-channel-power? l0-types:power-dbm
| +--rw preferred-rx-channel-power? l0-types:power-dbm
+--rw gsnr-extra-margin? snr
+--rw use-regen? boolean
+--rw wavelength-conversion? boolean
+--rw wavelength-assignment? identityref
+--rw guard-band-size? l0-types:frequency-thz
+--rw matching-fwd-rev-wavelength? boolean
+--rw allow-retuning? boolean
+--rw delta-power? l0-types:power-ratio
Tunnel-scope
augment /te:te/te:tunnels/te:tunnel/te:primary-paths
/te:primary-path/te:explicit-route-objects
/te:route-object-exclude-always/te:type
/te:numbered-node-hop/te:numbered-node-hop:
+--rw path-in-transceiver
| +--rw transponder-id? uint32
| +--rw transceivers* [lane-id]
| +--rw lane-id uint8
| +--rw transceiver-id? uint32
| +--rw operational-modes* string
| +--rw tx-tune-constraints
| | +--rw min-central-frequency? frequency-thz
| | +--rw max-central-frequency? frequency-thz
| | +--rw transceiver-tunability? frequency-ghz
| +--rw line-coding-bitrate* identityref
| +--rw tx-channel-power? l0-types:power-dbm
| +--rw preferred-rx-channel-power? l0-types:power-dbm
+--rw path-out-transceiver
+--rw transponder-id? uint32
+--rw transceivers* [lane-id]
+--rw lane-id uint8
+--rw transceiver-id? uint32
+--rw operational-modes* string
+--rw tx-tune-constraints
| +--rw min-central-frequency? frequency-thz
| +--rw max-central-frequency? frequency-thz
| +--rw transceiver-tunability? frequency-ghz
+--rw line-coding-bitrate* identityref
+--rw tx-channel-power? l0-types:power-dbm
+--rw preferred-rx-channel-power? l0-types:power-dbm
Path-scope

## Slide 4: Updated WDM Label Specifications
WSON
  DWDM fixed-grid and CWDM
Flexi-grid
Single vs. Multi-carrier
augment /te:te/te:globals/te:named-path-constraints
/te:named-path-constraint/te:explicit-route-objects
/te:route-object-include-exclude/te:type/te:label
/te:label-hop/te:te-label/te:technology:
+--:(wdm)
+--rw (grid-type)?
+--:(fixed-dwdm)
| +--rw (fixed-single-or-super-channel)?
| +--:(single)
| | +--rw dwdm-n? l0-types:dwdm-n
| +--:(multi)
| +--rw subcarrier-dwdm-n* l0-types:dwdm-n
+--:(cwdm)
| +--rw cwdm-n? l0-types:cwdm-n
+--:(flexi-grid)
+--rw (single-or-super-channel)?
+--:(single)
| +--rw flexi-n? l0-types:flexi-n
| +--rw flexi-m? l0-types:flexi-m
x--:(super)
| x--rw subcarrier-flexi-n* [flexi-n]
| +--rw flexi-n l0-types:flexi-n
| +--rw flexi-m? l0-types:flexi-m
+--:(multi)
+--rw frequency-slots
+--rw frequency-slot* [flexi-n]

## Slide 5: Open Issues
Draft text needs proper updates to align with the WDM tunnel YANG model updates
Modeling of 3R in alignment with OI vs. service function : pros/cons
The intension is to use this model as SDN controller NBI to support tunnel provisioning for both integrated transponder (e2e) and remote transponder (book-ended).
In the case of remote DWDM interface hosted in packets devices the expectation is to adopt the model as NBI for both IP and Optical controllers. Further gap analysis is needed to ensure this model can coverage of all the scenarios
Need to discuss how to model the relationship between a WDM tunnel and the resultant OTSi/OTSiG after the WDM tunnel is instantiated.

## Slide 6: Open Issues
Draft text needs proper updates to align with the YANG model changes
How to model attributes that are at the boundary of L0/L1, e.g. OUT types, OTU/ODU payload handling at regen node
Modeling of 3R regens as service functions: pros/cons and how
The intension is to use this model as SDN controller NBI to support tunnel provisioning for both integrated transponder (e2e) and pluggables (book-ended). In the case of pluggables the expectation is to use the model as NBI for both IP and optical controller. Gap analysis is needed to ensure that this model can coverage of all the scenarios
Need to discuss how to model the relationship between a WDM tunnel and the resultant OTSi/OTSiG after the WDM tunnel is instantiated. Also relevant to discuss whether OTSi and OTSiG information in the optical impairment model are still needed

## Slide 7: Next Steps and Actions
Address open issues aforementioned
Seek feedback from the WG and especially from operators and implementers
Perform gap analysis of this model in the context of pluggables use cases
  Weekly team meeting:
    Thursday, 14:00 (CET)
    CCAMP WebEx Details
      https://ietf.webex.com/ietf/j.php?MTID=ma1ca3bcec716fe1ff93e0a28b3558294
      Join by meeting number
        Meeting number (access code): 2422 698 1495
        Meeting password: 6UbM2tEJJd6

## Slide 8: YANG Data Models for requesting Path Computation in WDM Optical Networks
Co-authors:
Aihua Guo (Futurewei)
Sergio Belotti (Nokia)
Italo Busi (Huawei)
Contributors:
Daniel King (Olddog Consulting)
draft-ietf-ccamp-optical-path-computation-yang-03
IETF 119, Brisbane

## Slide 9: Summary of Updates in -03 Rev.
Introduced a combined YANG data model for path computation on WSON and flexi-grid WDM networks
  YANG module renamed as ietf-wdm-path-computation (prefix: wdm-pc); obsoleted wson-pc and flexg-pc
YANG model updates:
  Aligned with WDM tunnel YANG by using the same constructs (global constraints on transceivers and 3R regens, etc.)
  Aligned with RFC9093-bis on the WDM label structure definitions
  Aligned with te-path-computation base model

## Slide 10: Open Issues
Should the draft be renamed to "WDM path computation to keep alignment with the WDM tunnel draft?
The intension is to use this model as SDN controller NBI to support tunnel path computation for both local transponder (e2e) and remote transponder (book-ended).
In the case of remote DWDM interface hosted in packets devices the expectation is to adopt the model as NBI for both IP and Optical controllers. Gap analysis is needed to ensure that this model can cover of all the scenarios

## Slide 11: Next Steps and Actions
Expand the list of co-authors contributors
Continue to align with WDM tunnel on the definitions
Seek feedback from the WG and especially from operators and implementers
Perform gap analysis of this model in the context of pluggables use cases
  Weekly team meeting:
    Thursday, 14:00 (CET)
    CCAMP WebEx Details
      https://ietf.webex.com/ietf/j.php?MTID=ma1ca3bcec716fe1ff93e0a28b3558294
      Join by meeting number
        Meeting number (access code): 2422 698 1495
        Meeting password: 6UbM2tEJJd6

## Slide 12: Thank you!