## Slide 1: Draft Review for IETF’116

## Slide 2: draft-srld-teas-5g-slicing-06
This is an informational draft that summarizes the realization of 5G slices over IP/MPLS networks using existing technologies. This draft may be of interest to the IP team.
This work is driven primarily by Juniper and various operators like Orange and Telefonica.
This draft focuses on 5G slicing mapping to an IETF network slice in the transport domain and describes how to use a single NRP to realize an IETF network slice. The NRP deals with fine-grained or coarse-grained resource control for VLAN/IP/label hand-off, 5G QoS mapping to DSCP and TE, etc.
The mapping and NRP realization for transport are totally different and 5G is not a direct use case for optical transport. Therefore, the realization method proposed in this draft does not apply to optical/OTN.

## Slide 3: Draft-ldbc-cats-framework-01
This is the initial framework document for Computing-Aware Traffic Steering. This work is currently driven by HW and operators.
This document describes the components and workflow between the control and data plane for traffic optimization between computing nodes and the network.
The CATS framework is an ingress-based overlay framework, and currently it assumes that all the edge computing nodes are in the same administrative domain, and the underlying network is a packet routed network. Therefore, it uses the famous overlay-underlay to basically run computing services over traditional IP/MPLS networks, which may be CATS-unaware.
Our work for optical-to-cloud is targeting similar applications using OTN/OSU as potential underlay networks. It may be beneficial to push the CATS framework document to not exclude using non-IP underlay infrastructure to support computing needs. Then it may worth to consider moving the optical-to-cloud work into the CATS WG.

## Slide 4: draft-peng-apn-scope-gap-analysis-06
This is an information draft for performing a gap analysis for solutions based on the concept of application-aware networking. This work is driven by HW IP.
The gap analysis claims that existing solutions in the IETF that identify client traffic for steering and optimization are specific to a particular scenario or data plane. APN requires much more fine-grained identification methods.
The entire APN work has overlaps with other work such as ALTO or CATS, and APN is currently not an active WG.

## Slide 5: draft-shi-cats-analysis-of-metric-distribution-00
This draft performs a gap analysis on methods for distributing computing metrics to the ingress router
This document is incomplete in that it only lists and compares four scenarios for deploying the metric collection agent and interacting with the controller. There is no gap analysis yet.

## Slide 6: draft-Contreras-alto-service-edge-07
This draft proposes an approach to distribute the information of computing and networking resources to applications like CDN networks to assist the selection of deployment locations of CDN nodes for optimized performance. This information is exposed under the framework of ALTO.
The defined information is for an application to consume. Currently I do not see a relevance of this work to our work, as to the best extent we may use application information to assist network operations, hence the other way around. However, depending on our involvement in the CATS there may be some synergy and process defined between computing applications and network. Hence suggest to passively follow up on this work.

## Slide 7: draft-Contreras-teas-slice-controller-models-05
This is an updated informational draft which describes the network slice controller reference architecture, and how it maps to the network slicing framework.
The most recent change describes the NS-mapper and NS-realizer in an NS controller, and maps the current model for NS NBI and OTN slicing onto the interface between the mapper and realizer. It also adds additional description to reference recent updates in using customized topologies.
Hence, this draft is a useful support to our drafts.

## Slide 8: Draft-janz-nmrg-performance-digital-twin-00
This is new draft on digital twin, driven by CRC and us.
The focus of this draft is to present the design and interface requirements for an optical performance digital twin (OPDT) based on past work on the optical behavior simulation.

## Slide 9: Draft-barguil-teas-network-slices-instantation-06
This daft is a realization document for network slices. It describes how to use L2SM, L3SM and network models (L2VPN, L3VPN) to realize an IETF network slice within a network controller.
This draft describes the workflow from network slice instantiation over a packet-based networks (L2/L3). Suggest to follow up on this work to understand the scenarios from operator’s perspective to realize network slices.

## Slide 10: Draft-liu-teas-transport-network-slice-yang-06
This is an updated draft driven by us to define an interface for specifying customized topologies used in network slicing
Next step is to push this draft into WG adoption to be used further by network slicing. There is still pending discussion on how the customized topology may be used and this document will provide the necessary steps.

## Slide 11: Draft-chen-nmrg-dtn-interface-01
This draft specifies the interface requirement for a generic network digital twin. This work is driven by China Mobile.
Since the other draft on performance digital twin also defines some design guidelines of a performance digital twin. It would be useful for the two drafts to work together towards a unified requirement document. Need to follow up on this work.

## Slide 12: NETMOD
Adaptive Subscription to YANG Notification
  https://datatracker.ietf.org/doc/html/draft-wang-netconf-adaptive-subscription-07
  Mechanism to reduce YANG notification overhead in networks with large amount of data notifications
Transaction ID Mechanism for NETCONF
  https://datatracker.ietf.org/doc/html/draft-lindblad-netconf-transaction-id-01
  Useful extensions for Netconf
List Pagination for YANG-driven Protocols
  https://datatracker.ietf.org/doc/html/draft-wwlh-netconf-list-pagination-00
  https://datatracker.ietf.org/doc/html/draft-wwlh-netconf-list-pagination-nc-02
  https://datatracker.ietf.org/doc/html/draft-wwlh-netconf-list-pagination-rc-02
  Server-side caching implementation. Useful extensions for Netconf client

## Slide 13: OPSAWG
SAIN (Service Assurance for Intent-based Networking)
  https://datatracker.ietf.org/doc/draft-ietf-opsawg-service-assurance-architecture/
  https://datatracker.ietf.org/doc/draft-ietf-opsawg-service-assurance-yang/
  Service assurance in directed graph, useful for root cause analysis
A YANG Model for Network and VPN Service Performance Monitoring
  https://datatracker.ietf.org/doc/draft-ietf-opsawg-yang-vpn-service-pm/
  PM defined augmenting ietf-network
    Relationship to our work on PM?
Data Manifest for Streaming Telemetry
  https://datatracker.ietf.org/doc/draft-claise-opsawg-collected-data-manifest/
  Useful for telemetry stream processing with context and metadata associated with the streaming data
A Network YANG Model for Service Attachment Points
  https://datatracker.ietf.org/doc/draft-dbwb-opsawg-sap/
  UNI renamed?
  How does it relate to the TTP concept in TE topology?
A YANG Data Model for Optical Network Inventory
  https://datatracker.ietf.org/doc/draft-yg3bp-ccamp-optical-inventory-yang/
  “Inventory” is overloaded?
  Need an interim meeting to discuss the scope

## Slide 14: TEAS
Network slicing

## Slide 15: RTG
Satellite communication
  Research projects?
  Matt’s Simulation results to show routing convergence works with traditional routing protocols
  MANET work is similar to this work
  Forwarding table is thrown away or not?
Cloud network from China Mobile
  Connection to the OTN network-to-cloud work?

## Slide 16: NETMOD
draft-ietf-netmod-yang-packages-01
  Schema mount restriction : mount point and mount schema constraints to be defined
draft-ma-netmod-with-system-00
  System defined configuration
  Allow user to customize attributes into the running and operational data store?