## Slide 1: IETF Network Slice Topology YANG Data Model
Co-authors:
Xufeng Liu (IBM)
Jeff Tantsura (Microsoft)
Igor Bryskin (Individual)
Luis M. Contreras (Telefonica)
Qin Wu (Huawei)
draft-liu-teas-transport-network-slice-yang-06
Sergio Belotti (Nokia)
Reza Rokui (Ciena)
Aihua Guo (Futurewei)
Italo Busi (Huawei)

## Slide 2: Motivation
A network slice may require an additional level of control to customize its connections, as described in Section 2 of draft-ietf-teas-ietf-network-slices.
  “Additionally, the IETF Network Slice service customer might ask for some level of control of, e.g., to customize the service paths in a network slice.”
A network slice can benefit from using a customized topology to allow better resource reservation and resource sharing among connections
  We call it a “network slice topology”

## Slide 3: Network Slice Topology
A network slice topology is a customized topology used to expresses a customer’s intent for reserving topology resources and expressing connectivity constraints
  A network slice topology is defined by the customer(“customized”), not one exposed by the provider(“abstract” or “native” topology)
  Existing topology models, e.g. network topology or TE topology is not intent driven, e.g. no customer SLO/SLEs defined
Service paths for connections in a network slice can be specified on top of a network slice topology
The topology model defined in early revisions of draft-liu-teas-transport-network-slice-yang is a good candidate for defining the network slice topology

## Slide 4: Updates in Rev-06
  Imported common SLO/SLE attributes from ns-nbi & applied them to the topology constructs
  Removed the augments from the TE topology model for model connectivity constructs as they are already covered by the ns-nbi YANG model
  Text & diagram updates

## Slide 5: Updated Model Relationships

## Slide 6: Model Tree
Network augments
Node augments

## Slide 7: Model Tree (Cont.)
Link augments
TP augments

## Slide 8: Open Issue
Should the NS-NBI model reference this topology model, or any topology model?
  Restrain that the topology to be reference is of type “network-slice”

## Slide 9: Next Steps
Resolve open issues
Request for WG adoption
* GitHub Repo
  https://github.com/aguoietf/ietf-network-slice-topology

## Slide 10
Thank You!